## Slide 1: Jefferson County Study on Bacterial Contamination of Drinking Water Wells
Carissa Caruso-DiPaolo
NEHA / CDC Intern
Environmental Science & Forestry
State University of New York – Syracuse
Josh Griffin, CPO-I
Sanitarian
Jefferson County Health Department
Bob Custard, RS, CP-FS, CPO-I
Environmental Health Consultant
Jefferson County Health Department

## Slide 2: Objectives of Study
Identify areas in Jefferson County with a high risk for biological groundwater contamination
Hypothesize reasons for why biological contamination is occurring

## Slide 3: Methodology
State lab data on 770 samples of water from private drinking water wells with physical addresses in Jefferson County was analyzed for the 7-year period from July 2012 through June 2019
Colilert test
  Wells positive for total coliform indicate surface water contamination
  Wells positive for E. Coli indicate fecal contamination
Only the data from the first sample from each location was used

## Slide 4: Limitations of this Study
A convenience sample (not random sampling)
Sampling error
Sample tampering
Inaccurate locations
  P.O. box addresses
  Illegible addresses on sample form
  Addresses of sampler rather than sample location
Sample size when looking at neighborhoods

## Slide 5: Jefferson County Well Contamination Study
Chart: 
| Safe Drinking Water | Contamination with Surface Water | Contamination with Surface Water & Feces
 | 416 | 269 | 85
N = 770

## Slide 6: What Did We Learn?
46% of the 770 drinking water wells were positive for total coliform bacteria, an indicator of groundwater contamination by surface water
11% of the 770 drinking water wells were contaminated with E. coli bacteria, an indicator of contamination with mammalian feces from septic systems, pets, wild animals, livestock, or application of manure or poultry litter
These both exceeded the average results from water samples taken by USGS from major aquifers throughout the U.S.

## Slide 7: What Did We Learn?
Chart: Well Contamination
| Total Coliform + (Probable Contamination by Surface Water) | E. coli + (Contamination with Mammalian Feces)
United States | 0.261 | 0.079
Jefferson County | 0.459 | 0.11039
Reference: DeSimone, L.A., Hamilton, P.A., and Gilliom, R.J., 2009, The quality of our nation’s waters—Quality of water from domestic wells in principal aquifers of the United States, 1991–2004—Overview of major findings: U.S. Geological Survey Circular 1332, 48 p.

## Slide 8: What Did We Learn?
Chart: Private Wells in Jefferson County, WV Percent Positive for Total Coliform Bacteria
| FY13 | FY14 | FY15 | FY16 | FY17 | FY18 | FY19
 | 0.45638 | 0.43137 | 0.44792 | 0.36364 | 0.40367 | 0.51429 | 0.61616

## Slide 9: What Did We Learn?
The percentage of samples positive for total coliform bacteria (indicating surface water contamination) has increased by 35% since FY13
Chart: Private Wells Total Coliform Bacteria Positive
| United States | Jefferson County FY13 | Jefferson County FY19
Total Coliform | 0.261 | 0.45638 | 0.61616
+35%

## Slide 10: What Did We Learn?
Chart: Private Wells in Jefferson County, WV Percent Positive for E. coli bacteria
| FY13 | FY14 | FY15 | FY16 | FY17 | FY18 | FY19
 | 0.060403 | 0.078431 | 0.10417 | 0.054545 | 0.11927 | 0.2 | 0.18182

## Slide 11: What Did We Learn?
The percentage of samples positive for E. coli bacteria (indicating mammalian fecal contamination) has increased by 203% since FY13
Chart: Private Wells E. coli Bacteria Positive
| United States | Jefferson County FY13 | Jefferson County FY19
E. coli | 0.079 | 0.060403 | 0.18182

## Slide 12: What Did We Learn?
Warmer months (April - October) had more fecal contamination than colder months (November - March)

## Slide 13: What Did We Learn?
Chart: Average Monthly Rainfall
| January | February | March | April | May | June | July | August | September | October | November | December
 | 2.48 | 2.2243 | 2.2757 | 2.9343 | 5.1 | 3.2157 | 3.9871 | 3.1571 | 3.69 | 3.6614 | 2.11 | 3.0314
There was some correlation between the average monthly rainfall and the percentage of samples that were E. coli positive.

## Slide 14: What Did We Learn?
The increase in the percentage of E. coli positive samples appears to not be entirely related to rainfall. The trend was occurring prior to the very heavy rainfall in FY19.
Chart: 
| FY13 | FY14 | FY15 | FY16 | FY17 | FY18 | FY19
Rainfall | 35.22 | 38.34 | 32.97 | 27.89 | 29.66 | 41.68 | 59.31
% E. coli + x3.32 | 20.0479 | 26.0224 | 34.5859 | 18.0896 | 39.5979 | 66.3837 | 60.3428

## Slide 15: Hypotheses That Didn’t Hold Water
“What gets us into trouble is not what we don't know. It's what we know for sure that just ain't so.”
- Mark Twain

## Slide 16: Hypothesis #1
In Jefferson County wells are more likely to be contaminated in areas with intensive agriculture

## Slide 17: South Agricultural Part of County
Some areas of intensive agriculture have little fecal contamination.

## Slide 19: Hypothesis #2
In Jefferson County, wells are more likely to be contaminated in karst areas

## Slide 20
What is Karst?
Karst is a topography formed from the dissolution of soluble rocks such as limestone or dolomite. It is characterized by underground drainage systems with sinkholes and caves. In karst areas contaminants can easily pollute groundwater and travel long distances quickly.

## Slide 22: Hypothesis #3
In Jefferson County wells are more likely to be contaminated in areas with steep slopes

## Slide 23
Shannondale

## Slide 24: Shannondale
N = 112

## Slide 25: Hypothesis #4
In Jefferson County wells are more likely to be contaminated in areas underlain by shale where the soils are most poorly suited for septic systems

## Slide 26
Area circled in red = area of shale bedrock

## Slide 27: Hypothesis #5
In Jefferson County wells are more likely to be contaminated in areas that are more densely populated

## Slide 28
Green = Rural (agricultural) zoning

## Slide 29: What Did We Learn?
Contamination was not concentrated in one area of Jefferson County, but several potential “hot spots” were identified

## Slide 30: Areas Which May Have a Higher Incidence of Well Contamination
Middleway
Wide Horizon Blvd
Steamboat Run
Brown’s Corner
West Huyett Road
Avon Bend
Blue Ridge Acres

## Slide 31: Study Conclusions
Wells in Jefferson County are more likely to have contamination from surface water and more likely to have fecal contamination than wells nationally
Over the last 7 years, there has been a significant increase in the percentage of wells that have tested positive for contamination

## Slide 32: Study Conclusions
Based on FY19 data, which showed that 61.6% of the wells tested were positive for total coliform bacteria, as many 17,000 persons in Jefferson County may be drinking water from wells subject to contamination by surface water
Based on FY19 data, which showed that 18.2% of the wells tested were positive for E. coli bacteria, more than 5,000 persons in Jefferson County may be drinking water from wells contaminated with fecal material

## Slide 33: How Will We Use This Data?
Targeted outreach to well owners in areas with a higher risk of groundwater contamination encouraging them to test their well water
General community education on protecting groundwater from contamination
Further study focused on identifying the sources of groundwater contamination

## Slide 34: Opportunities for Further Research
Analysis of data by:
  Rainfall patterns
  Well depth
  Well age
  Proximity to failing septic systems
Concentrated sampling in specific high-risk neighborhoods
Sampling for other contaminants
  Nitrates
  Arsenic
  Pesticides
  Lead
  VOCs

## Slide 35: Our Thanks To …
Kearneysville District Environmental Laboratory West Virginia Department of Health
  Brenda Hall, Lab Director
  Brad Kincheloe, Microbiologist II
  Julie McGhee, Microbiologist I
National Environmental Health Association
  Christine Ortiz Gumina, Project Coordinator
Environmental Health Services Branch, Centers for Disease Control & Prevention

## Slide 36: Questions?

## Slide 37: Speaker Contact Information:
Carissa Caruso-DiPaolo
NEHA / CDC Intern
ccarusod@syr.edu
Josh Griffin, CPO-I
Jefferson County Sanitarian
Joshua.W.Griffin@wv.gov
(304) 728-8416
Bob Custard, RS, CP-FS, CPO-I
Environmental Health Consultant
Robert.W.Custard@wv.gov
(304) 728-8416